www.efiexpert.com

21575 Apple Hill Dr.

Sonora, CA 95370

209-247-6497

MSD Distributor Conversion

to CAM Sync Instructions:

The CAM sync pulse must happen before the crank pulse on cylinder #1 firing stroke.  Since this conversion ONLY provides the CAM sync signal the crankshaft reference signal must come from another source such as a crank trigger.  Since the crankshaft reference should occur at 50-60 degrees this conversion will generate the cam sync pulse well before that.

The timing of this CAM sync pulse is not critical.  It can occur anywhere from 60-90 degrees BTDC on cylinder #1 for FAST and about 195 degrees for Holley. See specific instructions for each ECU type.

Conversion:

The MSD distributor must be disassembled and the reluctor removed. Grind off 7 teeth. The remaining tooth will be the can sync pulse, so pay attention to which terminal will become cylinder #1 firing.

Installation after conversion was done:

1) Set the engine to about 25 degrees BTDC on cylinder #1.  Make sure it’s the compression stroke.

2) Install this distributor and rotate to point the rotor directly at the #1 terminal. Since the rotor is locked out, this allows the timing from the ECU to adjust from 10 degrees to 40 degrees without the rotor ever being out of phase.

3) Lock down the distributor.

4) Manually rotate the engine to make sure that the cam signal will happen at the correct timing location. There is no need to ever move the distributor from this point on.

In the EFI software make sure the cam sensor input is set to inductive or magnetic, and sequential injection.